MATERIAL SAFETY DATA SHEET

| Effective Date | May 15, 2002 |
| --- | --- |
| MSDS Number | M49 |

Section 1 – Product and Company Information

| Product Name: | 4A Molecular Sieve |
| --- | --- |
| Product Use: | Desiccant, absorbent |
| Grades: | 4A |
| Synonyms: | Synthetic zeolite |
| Company; | Multisorb Technologies, Inc. |
| Street Address: | 325 Harlem Road |
| City, State, Zip, Country: | Buffalo, NY 14224-1893 USA |
| Telephone Number: | (716) 824 8900 [USA] Monday - Friday (8:00 - 5:00 EDT) |
| Fax Number: | (716) 824 4091 [USA] |
| Website / E-Mail : | multisorb.com |

Section 2 – Composition / Information on Ingredients

| Component Name | CAS Number | % by Weight |  |
| --- | --- | --- | --- |
| Sodium oxide (synthetic) Na2O | 1313-59-3 | ( 30 |  |
| Magnesium oxide MgO | 1309-48-4 | ( 5 |  |
| Aluminum oxide (non - fibrous ) Al2O3 | 1344-28-1 | ( 30 |  |
| Silicon oxide ( Synthetic ) SiO2 | 7631-86-9 | ( 50 |  |
| Quartz SiO2 ( Crystalline ) 14808-60-7 ( 3 |
| While this material is not classified as hazardous under OSHA regulations, this MSDS contains valuable information critical to the safe handling and proper use of this product. This MSDS should be retained and available for employees and other users of the product. |

Section 3 – Hazard Identification

| Emergency Overview: | This product is odorless, tan pellets, granules, beads, white powder or cake. This product is not combustible. When first wetted this product can heat up to the boiling point of water. Flooding with water will reduce the temperature. |
| --- | --- |
| Potential Health Effects: |  |
| Eyes: | Dust and or product may cause eye discomfort and irritation seen as tearing and reddening. |
| Skin: | The product dust may cause drying of the skin. This material becomes hot when it first comes in contact with moisture. The hot material could cause thermal burns. |
| Ingestion: | This product gets hot as it absorbs water. Burns to moist body tissue can result if contact is prolonged. |
| Inhalation: | Inhalation of the dust may cause irritation of the respiratory tract. Irritation may be accompanied by coughing and chest discomfort. |
| Medical Effects Generally Aggravated by Exposure: | Respiratory ailments |
| Chronic Effects/Carcinogenity: | Prolonged inhalation of powder fines may cause lung damage. Molecular sieve is not a carcinogen but molecular sieve may contain up to 3 % quartz which is classified as a suspected human carcinogen according to ACGIH. |

Carcinogenity Classification

International Agency for Research on Cancer (IARC)   Silicon oxide (synthetic ) - Unclassifiable as to carcinogenity in humans ( Group 3 ).  Chronic inhalation of crystalline silica gel in the form of quartz from occupational sources is carcinogenic to humans ( Group 1 ).

U. S. National Toxicology Program (NTP)   Quartz - Known human carcinogen when used as a condition of chronic exposure.

U. S. Occupational Safety and Health Administration (OSHA)    Quartz - known carcinogen when used as a condition of chronic exposure.

American Conference of Government Industrial Hygienists (ACGIH)   Aluminum oxide - Not classified as a human carcinogen (A4).  Quartz Suspected human carcinogen (A2) when used as a condition of chronic exposure.

Section 4 – First Aid Measures

| Eyes: | Rinse the eyes well with water while lifting the eye lids. If irritation persists, consult a physician. |
| --- | --- |
| Skin: | Wash affected area with soap and water. |
| Ingestion: | Ingestion is unlikely, however, if ingested in large quantities, drink (2) glasses of water which will cool the molecular sieve. Contact physician for permission to induce vomiting. This product gets hot as it adsorbs moisture. Burns to moist body tissue can result if contact is prolonged. No other evidence of adverse effects from available information. |
| Inhalation: | Remove the affected person to fresh air and get medical attention if necessary. |
| Notes to Physician: | This material gets hot enough to cause the burning of tissue when it adsorbs moisture. For this reason we always recommend rinsing with water to cool the molecular sieve. |

Section 5 – Fire Fighting Measures

| Flammable Properties: | Not flammable |
| --- | --- |
| Flash Point: | Not applicable | Method: | Not applicable |
| Flammable Limits: |  |
| Lower Flammability Limit: | Not applicable |
| Upper Flammability Limit: | Not applicable |
| Autoignition Temperature: | Not applicable |
| Hazardous Combustion Products: | None |
| Extinguishing Media: | Use extinguishing media that is appropriate for the surrounding fire. Molecular sieve is not combustible. |
| Fire Fighting Instructions: | Not combustible. |
| Unusual Fire and Explosion Hazards: | Molecular sieve will get hot enough to burn tissue when it adsorbs moisture rapidly. Use an excess of water to cool the molecular sieve. |

Section 6 – Accidental Release Measures

| Spill: | Sweep or vacuum up and place the spilled material in a waste disposal container. Avoid raising dust. Wash with soap and water after handling. |
| --- | --- |

Section 7 – Handling and Storage

| Handling: | Avoid raising dust and minimize the contact between the worker and the material. Practice good hygienic work practices. |
| --- | --- |
| Storage: | Store in a cool, dry location. Keep in sealed containers away from moisture. The molecular sieve will readily adsorb moisture. |

Section 8 – Exposure Controls/Personal Protection

| Engineering Controls: | Use exhaust ventilation to keep the airborne concentrations below the exposure limits. Ensure adequate ventilation, especially in confined areas. |
| --- | --- |
| Respiratory Protection: | Use NIOSH approved respirator when the air quality levels exceed the TLV's. |
| Skin Protection: | Light gloves will protect against abrasion and drying. |
| Eye Protection: | Safety glasses. |
| Component Name | Exposure Limits |  |
|  | OSHA PEL | ACGIH TLV | Other Recommended Limits |
| Sodium oxide | Not applicable | Not applicable | Not applicable |
| Magnesium oxide Aluminum oxide Silicon oxide Quartz | TWA 15 mg / m3 (fume, total particulate) TWA 15 mg / m3 (total dust as silicon) TWA 5 mg / m3 (respirable dust) TWA 15 mg / m3 (total dust as silicon) TWA 5 mg / m3 (respirable dust as silicon) TWA 250 mppcf / (SiO2 ( 5) (Crystalline quartz respirable) TWA 10 mg / m3 / (SiO2 ( 2) (Crystalline quartz respirable) TWA 30 mg / m3 / (SiO2 ( 2) | TWA 10 mg / m3 (fume) TWA 10 mg / m3 (total particulate matter) 10 mg / m3 (as silicon) TWA .05 mg / m3 (respirable dust) | IDLH 750 mg / m3 Not applicable TWA 10 mg / m3 (total dust as silicon) TWA 5 mg / m3 (respirable dust as silicon) NIOSH REL Ca TWA .05 mg / m3 IDLH Ca TWA .05 mg / m3 (Quartz) |

Section 9 – Physical and Chemical Properties

| Appearance: | Tan beads to a white powder | Vapor Density: | Not applicable |
| --- | --- | --- | --- |
| Odor: | None | Boiling Point: | Not applicable |
| Physical State: | Solid bead to powder | Melting Point: | Not applicable |
| PH: | Aqueous slurry 8 to 11 | Solubility: | Not soluble in water |
| Vapor Pressure: | Not applicable | Specific Gravity: | 2.1 |

Section 10 – Stability and Reactivity

| Stability: | Stable |
| --- | --- |
| Conditions to avoid: | Moisture and high humidity environments |
| Incompatibility: | Water, acids |
| Hazardous Decomposition Products: | None |
| Hazardous Polymerization: | Will not occur |

Section 11 – Toxicological Information

Animal Toxicology LD50/ oral / rat = (32,000 mg / kg( LD50 / dermal / rabbit = ( 2,000 mg / kg( LC50 / inhalation / rat = No data available Chronic toxicity Classification of ingredients EC Carcinogenic Not listed EC Mutagenic Not listed EC Toxic for Reproduction Not listed Carcinogenity (ACGIH) A4 (Aluminum oxide) A2 (Quartz) IARC classification Group 3 (Silicon oxide - synthetic) Group 1 (Quartz) Routes of exposure Exposure may occur via inhalation, contact with the skin and eyes. Irritation Not available Skin (rabbit) Not classified ass a skin irritant in animal testing( Eye (rabbit) Moderate eye irritation( Additional product information (The toxicology data has been taken from products of similar composition. Additional component information No data available.

Section 12 – Ecological Information

Mobility No data available. Biodegradation No data available. Bioaccumulation No data available. Aquatic toxicity No data available. Further information No information available.

Section 13 – Disposal Information

Disposal information If this product as supplied becomes a waste, it does not meet the criteria of a hazardous waste as defined under the Resource Conservation and Recovery Act (RCRA) 40 CFR 261. Materials of a hazardous nature that contact the product during normal use may be retained on this product. The user of the product must identify the hazards associated with the retained material in order to assess the waste disposal options. Dispose according to federal, state and local regulations.

Section 14 – Transportation Information

| Proper shipping name | NotNoffffwd |
| --- | --- |

UN - No.   Not applicable

Packaging Group   Not applicable

U.S. Dot   Not regulated

DOT Shipping Name   Not applicable

Hazard classification   Not applicable

IMO   Not regulated

EmS   Not applicable

MFAG   Not applicable

Marine pollutant   No

ICAO - IATA   Not regulated

Instruction passenger   Not applicable

Instruction cargo   Not applicable

Further information   Not classified as hazardous or dangerous in the meaning of transportation regulations.

Section 15 – Regulatory Information (Not meant to be all inclusive - selected regulations represented)

TSCA Listed: All of the ingredients of this mixture are on the TSCA substance inventory.

CERCLA (Comprehensive Environmental Response, Compensation and Liability Act) Reportable Quantity None of the component(s) of this product is / are subject to the release reporting under 40 CFR302 when release exceeds the reportable quantity (RQ). SARA Title III (Superfund Amendments and Reauthorization Act of 1986) Section 302 (Extremely Hazardous Substances) None of the component(s) of this product is / are subject To the emergency planning provisions of 40 CFR 355 when there are amounts equal to or greater than the Threshold Planning Quantity (TPQ). Section 313 (Toxic Chemicals) None of the component(s) of this product have been specified as Toxic Chemicals under SARA Section 313 and are not subject to the Toxic Release Inventory reporting requirements under 40 CFR 372. The following components are listed in the U.S. State Regulations. California - Proposition 65 Crystalline silica Massachusetts Right-to-Know Aluminum oxide, quartz New Jersey Right-to-Know Amorphous silica, aluminum oxide, magnesium oxide, silica (quartz). Pennsylvania Right-to-Know Silica, aluminum oxide, magnesium oxide, quartz OSHA PEL - Molecular sieve is not listed. See section 2 for the ingredients. NIOSH Molecular sieve is not listed. See section 2 for the ingredients. ACGIH Molecular sieve is not listed. See section 2 for the ingredients. USDA Not applicable FDA Not applicable Canadian Hazardous Products Act This product is classified as a material causing other toxic effects, Carcinogenity - Class D, Division 2, Subdivision A, under regulations pursuant to the Federal Hazardous. Canadian Environmental Protection Act All ingredients of this mixture are notified to CEPA and on the DSL Domestic Substances List). European Inventory of Existing Commercial Chemical Substances All components of this product are included in EINECS/ELINCS. Council of European Communities Directive on Classification, Packaging and Labeling of Dangerous Substances / Preparation (67/548/EEC & 88/379/EEC) No dangerous goods labels required.

Section 16 – Other Information

| HMIS – Hazardous Materials Identification System |
| --- |
|  | HMIS Rating |  |
|  | Health Flammability Reactivity | 1 (slight) 0 1 (slight) |  |

0 - minimal hazard, 1 - slight hazard, 2 - moderate hazard, 3 - serious hazard, 4 - severe hazard

This MSDS was prepared by:    George E. Mckedy

Senior Applications Development Specialist

Multisorb Technologies, Inc.

This data and recommendations presented in this data sheet concerning the use of our product and the materials contained therein are believed to be correct but does not purport to be all inclusive and shall be used only as a guide.  However, the customer should determine the suitability of such materials for his purpose before adopting them on a commercial scale.  Since the use of our products is beyond our control, no guarantee, expressed or implied, is made and no responsibility assumed for the use of this material or the results to be obtained therefrom.  Information on this form is furnished for the purpose of compliance with Government Health and Safety Regulations and shall not be used for any other purposes.  Moreover, the recommendations contained in this data sheet are not to be construed as a license to operate under, or a recommendation to infringe, any existing patents, nor should they be confused with state, municipal or insurance requirements, or with national safety codes.